__v16si vector addition on x86_64, 32-bit instructions only
MOV EAX, [VAR1+0] MOV EAX, [VAR1+32]
MOV EBX, [VAR1+4] MOV R9D, [VAR1+36]
MOV ECX, [VAR1+8] MOV R10D, [VAR1+40]
MOV EDX, [VAR1+12] MOV R11D, [VAR1+44]
MOV ESI, [VAR1+16] MOV R12D, [VAR1+48]
MOV EDI, [VAR1+20] MOV R13D, [VAR1+52]
MOV EBP, [VAR1+24] MOV R14D, [VAR1+56]
MOV R8D, [VAR1+28] MOV R15D, [VAR1+60]
ADD [VAR2+0], EAX ADD [VAR2+32], EAX
ADD [VAR2+4], EBX ADD [VAR2+36], R9D
ADD [VAR2+8], ECX ADD [VAR2+40], R10D
ADD [VAR2+12], EDX ADD [VAR2+44], R11D
ADD [VAR2+16], ESI ADD [VAR2+48], R12D
ADD [VAR2+20], EDI ADD [VAR2+52], R13D
ADD [VAR2+24], EBP ADD [VAR2+56], R14D
ADD [VAR2+28], R8D ADD [VAR2+60], R15D

---
 __v16si vector addition, MMX instructions: 64-bit SIMD
MOVQ MM0, [VAR1+0]
MOVQ MM1, [VAR1+8]
MOVQ MM2, [VAR1+16]
MOVQ MM3, [VAR1+24]
MOVQ MM4, [VAR1+32]
MOVQ MM5, [VAR1+40]
MOVQ MM6, [VAR1+48]
MOVQ MM7, [VAR1+56]
PADDD MM0, [VAR2+0]
PADDD MM1, [VAR2+8]
PADDD MM2, [VAR2+16]
PADDD MM3, [VAR2+24]
PADDD MM4, [VAR2+32]
PADDD MM5, [VAR2+40]
PADDD MM6, [VAR2+48]
PADDD MM7, [VAR2+56]
MOVQ [VAR2+0], MM0
MOVQ [VAR2+8], MM1
MOVQ [VAR2+16], MM2
MOVQ [VAR2+24], MM3
MOVQ [VAR2+32], MM4
MOVQ [VAR2+40], MM5
MOVQ [VAR2+48], MM6
MOVQ [VAR2+56], MM7
Available since Intel® Pentium® MMX (1997)

---
  __v16si vector addition, SSE2 instructions: 128-bit SIMD
MOVDQU XMM0, [VAR1+0]
MOVDQU XMM1, [VAR1+16]
MOVDQU XMM2, [VAR1+32]
MOVDQU XMM3, [VAR1+48]
PADDD XMM0, [VAR2+0]
PADDD XMM1, [VAR2+16]
PADDD XMM2, [VAR2+32]
PADDD XMM3, [VAR2+48]
MOVDQU [VAR2+0], XMM0
MOVDQU [VAR2+48], XMM1
MOVDQU [VAR2+16], XMM2
MOVDQU [VAR2+32], XMM3
Available since Intel® Pentium® 4 (2001), mandatory in all x86_64 processors (by ABI)
XMM registers first appeared in SSE (Pentium Ⅲ, 1999), but epi32 operations need SSE2.

---
  __v16si vector addition, AVX2 instructions: 256-bit SIMD
VMOVDQU YMM0, [VAR1+0]
VMOVDQU YMM1, [VAR1+32]
VPADDD YMM0, [VAR2+0]
VPADDD YMM1, [VAR2+32]
VMOVDQU [VAR2+0], YMM0
VMOVDQU [VAR2+32], YMM1
Available since Haswell microarchitecture (2013)
YMM registers first appeared in AVX (Sandy Bridge, 2011), but epi32 operations need AVX2.

---
__v16si vector addition, AVX-512F instructions: 512-bit SIMD
VMOVDQU ZMM0, [VAR1+0]
VPADDD ZMM0, [VAR2+0]
VMOVDQU [VAR2+0], ZMM0
Available since Intel® Xeon Phi™ x200 (2016) and Cannonlake microarchitecture (2017)
AVX-512DQ is not needed for these epi32 operations.

---
text